## Slide 1: Bento Packaging Activity Recognition with Convolutional LSTM using Autocorrelation Function and Majority Vote
Atsuhiro FUJII, Kazuki YOSHIDA, Kiichi SHIRAI, Kazuya MURAO
Ritsumeikan University, Japan

## Slide 2: Dataset (1/3)
Four subjects had attached one motion capture system with 29 markers.
The markers may be labeled incorrectly in some cases due to the complex setting.
https://abc-research.github.io/bento2021/data/

## Slide 3: Dataset (2/3)
Activity name | Movement direction pattern | Activity label
Normal | Inward | 1
 | Outward | 2
Forgot to put ingredients | Inward | 3
 | Outward | 4
Failed to put ingredients | Inward | 5
 | Outward | 6
Turn over bento-box | Inward | 7
 | Outward | 8
Fix/rearranging ingredients | Inward | 9
 | Outward | 10
The measurement time for each file ranges from 50 to 70 s.

## Slide 4: Dataset (3/3)
Subject | Activity label | # of segment | Length |  | 
 |  |  | max | mean | min
1 | 1~10 | 49 | 6962 | 5818 | 5516
2 | 1~10 | 52 | 8441 | 6303 | 6343
3 | 1~10 | 50 | 6337 | 5514 | 5459
4 | Unknown | 48 | 5947 | 5024 | 5481

## Slide 5: Method – Preprocessing (Overall)

## Slide 6: Method – Preprocessing (Converting process)
This process convert to velocity data from the raw data.
First, the process interpolate the missing values in the raw data.
Next, the interpolated data was used to calculate the velocity data.
500
300
100
900
700
The dataset frequency was 100 Hz.

## Slide 7: Method – Preprocessing (Partitioning process)
This process of divide the given data of approximately 60 s into data for one operation.
Sum
Autocorrelation
function
Time-series
velocity data
One file
Synthetic wave
One file
One operation
time-series
velocity data
files